Name: KEY									Id#

COE 205, Term 071

Computer Organization & Assembly Programming

Quiz# 1

Date: Monday, Sep. 24, 2007

# Q1. Fill the blank in each of the following questions:

## The program that translates assembly language into machine language is called assembler.

## There is a one-to-one mapping between assembly language and Machine Language.

## Two of the reasons for why it is important to program in Assembly Language are   accessibility to system hardware and space and time efficiency.

## Two advantages of programming in high-level language are program development is faster and maintenance is easier      and   programs are portable.

## The Instruction Pointer (IP) register holds the address of the next instruction to be fetched from memory.

## The Instruction Set Architecture (ISA) of a computer consists of instruction set, memory, and programmer-accessible registers.

## The Instruction Set Architecture provides an interface between hardware and software.

## The CPU is divided into two main units called Data Path unit and Control unit.

## With an address bus size equal to 36 bits, the memory address space is 236=64 G Bytes.

## With a data bus size equal to 64 bits, the maximum number of bytes that is transferred between the CPU and memory per a read/write cycle is   8 Bytes.

## In Volatile memory, data is lost when device is powered off while Non-Volatile memory stores information permanently.

## In static RAM, each cell is made up of 6 transistors and it is faster but less dense than dynamic RAM.

## The need for memory hierarchy is due to Processor-Memory Performance Gap.

## The Cache memory is faster than RAM and slower than registers.

## Given a magnetic disk with the following properties:

  - Rotation speed = 7200 RPM (rotations per minute)

  - Average seek = 8 ms, Sector = 512 bytes, Track = 200 sectors

Then, Time of one rotation (in milliseconds) = 1000/(7200/60)=1000/120 = 8.33 ms

Average time to access a block of 64 consecutive sectors = 8 + 0.5*8.33 + (64/200) * 8.33 = 8 + 4.17+2.66=14.83 ms

## The 6-bit binary number 110100 in sign-magnitude representation represents the decimal value -20 while in 1's complement representation it represents the decimal value -11 and in 2's complement representation it represents the decimal value -12.

## Assuming 8-bit 2's complement representation, the largest positive number that can be stored in decimal is +127 and in binary it is 0111 1111 while the smallest number that can be stored in decimal is -128 and in binary is 1000 0000.

## Assuming 8-bit 2's complement representation, the following operation A9 – 70 produces the results A9+90=39 and the overflow flag will be equal to 1.