Name:									Id#

COE 205, Term 011

Computer Organization & Assembly Programming

Quiz# 2

Date: Saturday, Oct. 6

# Suppose that you have the following initial content of the Intel 8086 registers:

AX=FA32H		BX=FFF0H		CX=FFFAH		IP =0FECH

SI   =0006H		DI =0005H		DS =2BF1H 		CS=1EADH

## Suppose that the following data segment is allocated in the segment given in the DS register with an offset of 0. Show the content of the allocated memory, and  determine the physical address of next instruction to be fetched from memory.  Note that the ASCII code of character `0` is 30H.

I 	DB	-80, `24`		     Address (Hex)    Memory Content (hex)

000A

DW	-50, `42`			  000B

DD	-255				  000C

L          EQU    128				  000D

J	DB	L-25				  000E

DW	offset I+16			  000F

K         DB	-1, 2 dup(4, 2 dup(-20))	  0010

M        DB	`Q#2$			 	  0011

0012

Address (Hex)    Memory Content (hex)	  0013

0000						  0014

0001						  0015

0002						  0016

0003						  0017

0004						  0018

0005						  0019

0006						  001A

0007						  001B

0008						  001C

0009						  001D

Physical address of next instruction to be fetched =

## Show the content of the registers and memory locations modified after the execution of each of the following instructions. Use the initial content of the registers and memory locations as initial values for the subsequent instructions. Furthermore, specify the addressing modes of the source and destination operands in each instruction.

### SUB CL,  BL

### MOV WORD PTR  J-1, offset I+2

### ADD [DI-3], AL

### MOV WORD PTR [BX+SI+14], L

## Write 8086 assembly code to ask the user to enter a lower case character and display it in upper case. Note that the ASCII code of character ‘A’ is 41h and that of ‘a’ is 61h.  A sample execution of the program is as follows:

## Enter a lower case character: h

## Character in upper case is: H