Name:									Id#

COE 205, Term 021

Computer Organization & Assembly Programming

Quiz# 2

Date: Monday, Oct. 28, 2002

# Q1. Analyze the 8086 assembly program given below and determine what it is doing. Determine exactly what the program will output, assuming that the input entered is 62.

.MODEL SMALL

.STACK 32

.DATA

CR       EQU    13

LF       EQU    10

msg1     DB     'Enter a 2-digit decimal number (00->99):','$'

msg2     DB     CR,LF, 'Result= '

result   DB     3 dup(?),'$'

.CODE

MOV AX, @DATA

MOV DS, AX

MOV DX, offset msg1

MOV AH, 9h

INT 21H

MOV AH, 1h

INT 21H

SUB AL, '0'

MOV BL, 10

MUL BL

MOV CL, AL

MOV AH, 1h

INT 21H

SUB AL, '0'

ADD AL, CL

MOV AH, 0

ADD AX, AX

DIV BL

ADD AH, '0'

MOV result+2, AH

MOV AH, 0

DIV BL

ADD AH, '0'

MOV result+1, AH

MOV AH, 0

DIV BL

ADD AH, '0'

MOV result, AH

MOV DX, offset msg2

MOV AH, 9h

INT 21H

MOV AX, 4C00h

INT 21H

END