Name:									Id#

COE 205, Term 033

Computer Organization & Assembly Programming

Quiz# 2

Date: Tuesday, July 6, 2004

# Q1. Represent the signed number -111 in sign-magnitude, 1’s complement and 2’s complement representations using the minimum number of bits possible.

# Q2. Find the decimal value of the following numbers:

## i.  (6A.4)16

## ii. (0110.0111)2

# Q3. Determine in both binary and decimal the range of values that can be represented in 6 bits for each of the following representations:

## unsigned representation

## sign-magnitude representation

## 1’s complement  representation

## 2’s complement  representation

# Q4. Assuming even parity show the 8-bit ASCII representation for each of the following characters: (Note that the ASCII code of character A is 41H and that of character 0 is 30H)

C:

4:

# Q5. Determine whether the following operations will produce correct results or not assuming 8-bit 2’s complement representation. Justify your answer.

## FF + 81

## 07F + 01

## FF + 7F