Name:									Id#

COE 205, Term 042

Computer Organization & Assembly Programming

Quiz# 2

Date: Sunday, March 6, 2005

# Q1. Consider an 8-bit register that has the binary number 11101110. Determine the decimal value of the number if it represents:

## An unsigned number.

## A signed number in sign-magnitude representation.

## A signed number in 1’s complement representation.

## A signed number in 2’s complement representation.

# Q2. Perform the following arithmetic operations assuming that numbers are represented using 8-bit 2’s complement representation. Indicate in your answer when an overflow occurs.

## i.  7F + FF

## ii. FE – 7F

# Q3. Fill the blanks in the following questions:

## (i)  The binary number 01100011 represents character _____________, and uses an ___________ parity bit. Note that the ASCII code of character A is 41H and that of character a is 61H.

## (ii) Assuming 8-bit 2`s complement representation, the smallest (negative) number is _________________ in binary and ____________ in decimal and the largest (positive) number is _________________ in binary and _________________ in decimal.

# (iii)  If you type the word A1a on your keyboard, the binary sequence sent to the computer using 8-bit ASCII code with the 8th bit being an even parity bit is _______________________________________________________________________. Note that the ASCII code for character 0 is 30H.