Name:									Id#

COE 205, Term 043

Computer Organization & Assembly Programming

Quiz# 2

Date: Tuesday, July 12, 2005

# Q1. Represent the numbers given below in Hexadecimal in the format specified in the table assuming 8-bits:

| Number | Sign-Magnitude | 1’s Complement | 2’s Complement |
| --- | --- | --- | --- |
| +73 |  |  |  |
| +59 |  |  |  |
| -73 |  |  |  |
| -59 |  |  |  |

## Q2. Using the 2’s complement Hexadecimal representation obtained in Q1, perform the following operations and indicate if an overflow occurs or not:

i. (-73) - (59)

ii. (73) + (-59)

## Q3. Determine the ASCII representation of the string ICS201 assuming Even Parity. Note that the ASCII code of character A is 41H and that of character 0 is 30H.