Name: KEY									Id#

COE 205, Term 051

Computer Organization & Assembly Programming

Quiz# 2

Date: Saturday, Oct. 1, 2005

# Q1. Represent the numbers given below in Hexadecimal in the format specified in the table assuming 8-bits:

| Number | Sign-Magnitude | 1’s Complement | 2’s Complement |
| --- | --- | --- | --- |
| +27 | 1B | 1B | 1B |
| +101 | 65 | 65 | 65 |
| -27 | 9B | E4 | E5 |
| -101 | E5 | 9A | 9B |

# Q2. Determine the range of numbers in both binary and decimal that can be represented assuming 8-bit 2’s complement representation.

Binary: 10000000  to 01111111

Decimal: -128         to     +127

## Q3. Using the 2’s complement Hexadecimal representation obtained in Q1, perform the following operations and indicate if an overflow occurs or not:

i. (-101) + (-27) = 9B + E5					9 B

+	E 5

------------

8 0 (-128)

There is no overflow as the result is correct. Note that the sign of the result is the same as the sign of the two operands.

ii. (101) - (-27) = 65 – E5 = 65 + 1B				6 5

+	1 B

------------

8 0 (-128)

There is overflow as the result is incorrect. Note that the sign of the result is NOT the same as the sign of the two operands.

## Q4. Determine in binary the ASCII representation of the string COE205 assuming Odd Parity. Note that the ASCII code of character A is 41H and that of character 0 is 30H.

## C	           O	     E		2	    0	         5

01000011     01001111    00100101      00110010    10110000    10110101