Name:									Id#

COE 205, Term 071

Computer Organization & Assembly Programming

Quiz# 2

Date: Saturday, Oct. 27, 2007

# Q1. Fill the blank in each of the following questions:

## The size of the address bus in the 8086 processor is _______ bits while in the Pentium IV Processor it is _________ bits.

## The size of the data bus in the 8086 processor is _______ bits while in the Pentium IV Processor it is _________ bits.

## The IA-32 registers consist of ________ 32-bit general-purpose registers, ________ 16-bit segment registers, the ______ register and the ____________________register.

## Adding the following two 16-bit numbers F0F8+EF8A has the following values on the flags: CF=______, ZF=______, SF=______, AF=______, PF=______, OF=______.

## The address of the instruction to be fetched is stored in a register called ___________________.

## After reading an instruction whose size is 64 bits, the instruction pointer is incremented by    ____________.

## Each machine language instruction is first fetched from memory and stored in _______________________.

## A processor is considered superscalar when ____________________________________________________________________.

## RISC processors have the following characteristics: _________________________, _________________________________, __________________________________, _____________________________________________________________________

## 16-bit and 8-bit parts of the registers ______, ______, ______, ______ can be accessed by programmers.

## With a 5-stage pipeline with each stage requiring one clock cycle for execution, the number of clock cycles needed to execute 10 instructions is ______________________.

## In real address mode, the staring address of segment#10CD is _____________ and the maximum ending address is _________________.

## In real address mode with a logical address given as 10A2:30A0, the linear address is __________________.

## In Flat Memory model, all segments are mapped to ____________________________________________ address space.

## In protected mode, linear address is translated to physical address using __________________.

## _____________________ provide information to the assembler while translating a program.

## Q2. Suppose that the following data declarations are allocated in the data segment.

I 	BYTE		 32, ‘32’

J	WORD		1234H, -10

K          EQU  		  1

ALIGN 4

L	DWORD	K-5

M         BYTE		2  dup(2, 2 dup(1))

## Show the content of the allocated memory, in hexadecimal.  Note that the ASCII code of character ‘A’ is 41H and that of ‘a’ is 61H. Also, the ASCII code of character ‘0’ is 30H.

| Variable | Memory Address (Hex) | Memory Content (Hex) |
| --- | --- | --- |
|  | 00404000 |  |
|  | 00404001 |  |
|  | 00404002 |  |
|  | 00404003 |  |
|  | 00404004 |  |
|  | 00404005 |  |
|  | 00404006 |  |
|  | 00404007 |  |
|  | 00404008 |  |
|  | 00404009 |  |
|  | 0040400A |  |
|  | 0040400B |  |
|  | 0040400C |  |
|  | 0040400D |  |
|  | 0040400E |  |
|  | 0040400F |  |
|  | 00404010 |  |
|  | 00404011 |  |
|  | 00404012 |  |

## Determine the content of destination registers after executing each of the given instructions:

## MOV AL, I+1

## MOV EBX, OFFSET J

## MOV CH, TYPE L

## MOV EDX, SIZEOF J

## MOV EDX, LENGTHOF J

## MOV DH, BYTE PTR J+1