Name:									Id#

COE 205, Term 082

Computer Organization & Assembly Programming

Quiz# 2

Date: Monday, March 23, 2009

# Q1. Consider an 8-bit register that has the binary number 10010110. Determine the decimal value of the number if it represents:

## An unsigned number.

## A signed number in 2’s complement representation.

# Q2. Perform the following arithmetic operations assuming that numbers are represented using 8-bit 2’s complement representation. Indicate in your answer when an overflow occurs.

## CB + CA

## 68 – E0

# Q3. Fill the blanks in the following questions:

## Assuming unsigned number representation, the hexadecimal number (8F)16 represents the decimal number ______.

## The decimal number 120 is represented in binary as ____________.

## The binary number 11000111 represents character __ and uses an ______ parity bit. Note that the ASCII code of character A is 41H and that of character a is 61H.

## Assuming 8-bit 2`s complement representation, the smallest (negative) number is ________________ in binary and _______ in decimal and the largest (positive) number is ________________ in binary and _______ in decimal.