Name:									Id#

COE 205, Term 991

Computer Organization & Assembly Programming
Quiz# 2

Date: Saturday, Oct. 7

# Suppose that you have the following initial content of the Intel 8086 registers:

AX=0312H		BX=0001H		CX=0010H		DX=0210H

SI   =0001H		DI =0002H		BP=0200H		SP  =0300H

DS =2000H		ES =3000H		CS=1000H		SS  =4000H

IP  =1220H

## Suppose that the following data segment is allocated in the segment given in the DS register with an offset of 0. Show the content of the allocated memory, and  determine the physical addresses of variables I and J. For memory addresses starting from variable K, just show the number of bytes allocated without showing the content.

I 	DB	8

DW	1234H

J	DB	10, 11

DW	offset J

K         DB	`Quiz#2`,`$`

## Show the content of the registers and memory locations modified after the execution of each of the following instructions. Use the modified contents of the registers and memory locations as initial values for the subsequent instructions. Furthermore, specify the addressing modes of the source and destination operands in each instruction.

### ADD AX,  word ptr I+1

### MOV DX, [offset J]

### ADD CX, [SI+1]

### MOV [BX+DI-1], BL

### MOV AX, word ptr I[BX]

### MOV J[BX][DI], CL

## Give on a separate line the string displayed on the screen by each of the following code fragments.

### MOV DX, offset K

MOV AH, 09H

INT 21H

### MOV DX, offset K+4

MOV AH, 09H

INT 21H

### MOV DL, K

MOV AH, 02H

INT 21H