Name:									Id#

COE 205, Term 992

Computer Organization & Assembly Programming
Quiz# 2

Date: Monday, Feb. 21

# Suppose that you have the following initial content of the Intel 8086 registers:

AX=FFF2H		BX=FFFFH		CX=0010H		DX=0210H

SI   =0004H		DI =0002H		BP=0200H		SP  =0300H

DS =53FFH		ES =EF00H		CS=5000H		SS  =4000H

IP  =1220H

## Suppose that the following data segment is allocated in the segment given in the DS register with an offset of 0. Show the content of the allocated memory, and  determine the physical addresses of variables I and J.

I 	DB	-88

DW	5432H, ‘12’

L          EQU    61

J	DB	L+3

DW	offset J

K         DB	`Q#1`,`$`

## Show the content of the registers and memory locations modified after the execution of each of the following instructions. Use the initial content of the registers and memory locations as initial values for the subsequent instructions. Furthermore, specify the addressing modes of the source and destination operands in each instruction.

### SUB AX,  WORD PTR  I+1

### MOV WORD PTR  I, offset J

### ADD AX, [DI-1]

### MOV BYTE PTR [BX+SI-1], L-1

## Give on a separate line the string displayed on the screen by each of the following code fragments.

### MOV DX, offset K

MOV AH, 09H

INT 21H

### MOV DX, offset K+2

MOV AH, 09H

INT 21H

### MOV DL, K

MOV AH, 02H

INT 21H