Name:									Id#

COE 205, Term 993

Computer Organization & Assembly Programming

Quiz# 2

Date: Sunday, June 25

# Suppose that you have the following initial content of the Intel 8086 registers:

AX=FAB1H		BX=00FFH		CX=FFFAH		IP =011AH

SI   =0003H		DI =0005H		DS =4AEBH 		CS =9000H

## Suppose that the following data segment is allocated in the segment given in the DS register with an offset of 0. Show the content of the allocated memory, and  determine the physical address of variable J.  Note that the ASCII code of character `A` is 41H.

I 	DB	-50, `AB`	 Address (Hex)        Memory Content (hex)

DW	`A`, `AB`

L          EQU    50

J	DB	L-25

DW	offset I+4

K         DB	2 dup( 2dup(15))

## Show the content of the registers and memory locations modified after the execution of each of the following instructions. Use the initial content of the registers and memory locations as initial values for the subsequent instructions. Furthermore, specify the addressing modes of the source and destination operands in each instruction.

### SUB AL,   J+4

### MOV WORD PTR  I+2, offset K+1

### ADD CH, [DI-3]

### MOV BYTE PTR [BX+SI-12], L-10

## Write an 8086 assembly program to (a) Ask the user to enter a character,  (b) Display the character in the middle of a box of 8 asterisks. Note that the ASCII code of LF is equal to 10 and that of CR is equal to 13.

Sample Execution:

Enter a character: C

***

*C*

***