Name: KEY									Id#

COE 205, Term 031

Computer Organization & Assembly Programming

Quiz# 2

Date: Tuesday, Oct. 7, 2003

# Q1. Consider an 8-bit register that has the binary number 10001100. Determine the decimal value of the number if it represents:

## An unsigned number.

= 128 + 8 + 4 = 140

## A signed number in sign-magnitude representation.

= - 12

## A signed number in 1’s complement representation.

The 1’s complement of 10001100 is 01110011 = 127-12= 115

So, the number 10001100 represents -115

## A signed number in 2’s complement representation.

The 2’s complement of 10001100 is 01110100 = 127-11= 114

So, the number 10001100 represents -114

# Q2. Perform the following arithmetic operations assuming that numbers are represented using 8-bit 2’s complement representation. Indicate in your answer when an overflow occurs.

## i. 1F + 5F

## 1

1  F

+	5  F

-------------

7  E

There is no overflow. We added two positive numbers and got a positive number.

## ii. 7F – F0

=  7F + 2’s complement of F0 = 7F + 10

7 F

+	1 0

-------------

8 F

There is overflow because we are adding two positive numbers and got a negative number.

# Q3. Fill the blanks in the following questions:

## (i)  The binary number 01100111 represents character _______g______, and uses an ____odd___ parity bit. Note that the ASCII code of character A is 41H and that of character a is 61H.

## (ii) Assuming 10-bit 2`s complement representation, the smallest (negative) number is ____1000000000___ in binary and ___-512_____ in decimal and the largest (positive) number is ___0111111111____ in binary and ____+511_____ in decimal.

# (iii)  If you type the phrase COE205 on your keyboard, the binary sequence sent to the computer using 8-bit ASCII code with the 8th bit being an even parity bit is ____11000011__11001111__1100101__10110010__00110000__00110101___________Note that the ASCII code for character 0 is 30H.