Name: KEY									Id#

COE 205, Term 032

Computer Organization & Assembly Programming

Quiz# 2

Date: Sunday, March 7, 2004

# Q1. Consider an 8-bit register that has the binary number 11100010. Determine the decimal value of the number if it represents:

## An unsigned number.

128 + 64 + 32 + 2 = 226

## A signed number in sign-magnitude representation.

- (64 + 32 + 2) = - 98

## A signed number in 1’s complement representation.

The 1’s complement is 00011101

So, the number is  -29

## A signed number in 2’s complement representation.

The 2’s complement is 00011110

So, the number is  -30

# Q2. Perform the following arithmetic operations assuming that numbers are represented using 8-bit 2’s complement representation. Indicate in your answer when an overflow occurs.

## i.  7F + 01

1

- F

+           0    1

---------------

- 0

There is overflow since the sign bit of the result is negative while it should be positive.

## ii. FE – 7F

# The 2’s complement of 7F is 81

F    E

+           8    1

---------------

- F

There is overflow since the sign bit of the result is positive while it should be negative.

# Q3. Fill the blanks in the following questions:

## (i)  The binary number 01000100 represents character _____D________, and uses an ____Even_______ parity bit. Note that the ASCII code of character A is 41H and that of character a is 61H.

## (ii) Assuming 7-bit 2`s complement representation, the smallest (negative) number is _____1000000______ in binary and ____-64_____ in decimal and the largest (positive) number is ___0111111____ in binary and _____+63_______ in decimal.

# (iii)  If you type the phrase Abc2 on your keyboard, the binary sequence sent to the computer using 8-bit ASCII code with the 8th bit being an even parity bit is ___01000001 11100010__01100011__10110010__. Note that the ASCII code for character 0 is 30H.