Name:									Id#

COE 205, Term 033

Computer Organization & Assembly Programming

Quiz# 2 Solution

Date: Tuesday, July 6, 2004

# Q1. Represent the signed number -111 in sign-magnitude, 1’s complement and 2’s complement representations using the minimum number of bits possible.

+111 = 1101111

-111 in sign-magnitude will be 11101111

-111 in 1’s complement will be 10010000

-111 in 2’s complement will be 10010001

# Q2. Find the decimal value of the following numbers:

## i.  (6A.4)16

= 6*16 + 10 + 4 * 16-1

= 106.25

## ii. (0110.0111)2

# = 1*2 + 1 * 22 + 1 *2-2 + 1*2-3 + 1*2-4

= 6 + 7/16

= 6.4375

# Q3. Determine in both binary and decimal the range of values that can be represented in 6 bits for each of the following representations:

## unsigned representation

range is from 0 to 26 – 1 = 0 to 63

range in binary is from 000000 to 111111

## sign-magnitude representation

range is from – (25 – 1)  to +(25 – 1) = -31 to +31

range in binary is from 111111 to 011111

## 1’s complement  representation

range is from – (25 – 1)  to +(25 – 1) = -31 to +31

range in binary is from 100000 to 011111

## 2’s complement  representation

range is from – (25)  to +(25 – 1) = -32 to +31

range in binary is from 100000 to 011111

# Q4. Assuming even parity show the 8-bit ASCII representation for each of the following characters: (Note that the ASCII code of character A is 41H and that of character 0 is 30H)

C:	11000011

4:	10110100

# Q5. Determine whether the following operations will produce correct results or not assuming 8-bit 2’s complement representation. Justify your answer.

## FF + 81	= 	80

Result is correct because we added two negative numbers and got a negative 			number.

-1 + (-127) = -128

## 7F + 01 = 	80

Result is incorrect because we added two positive numbers and got a negative 			number.

+127 + 1 = 128 which cannot be represent in 8-bits and is not equal to 80h=-128.

## FF + 7F =	7E

Result is correct because we added a positive number with a negative number and 		overflow can never occur.

# -1 + 127 = 126