Name: KEY									Id#

COE 205, Term 043

Computer Organization & Assembly Programming

Quiz# 2

Date: Tuesday, July 12, 2005

# Q1. Represent the numbers given below in Hexadecimal in the format specified in the table assuming 8-bits:

| Number | Sign-Magnitude | 1’s Complement | 2’s Complement |
| --- | --- | --- | --- |
| +73 | 49H | 49H | 49H |
| +59 | 3BH | 3BH | 3BH |
| -73 | C9H | B6H | B7H |
| -59 | BBH | C4H | C5H |

## Q2. Using the 2’s complement Hexadecimal representation obtained in Q1, perform the following operations and indicate if an overflow occurs or not:

- (-73) - (59)  = B7H – 3BH = B7H + C5H

B 7

+	C 5

------

7 C

There is overflow because the two operands are negative and the result is positive

ii. (73) + (-59)  = 49H + C5H

4 9

+	C 5

------

0 E

There is no overflow because the operation is effective subtraction which cannot produce overflow.

## Q3. Determine the ASCII representation of the string ICS201 assuming Even Parity. Note that the ASCII code of character A is 41H and that of character 0 is 30H.

## I		      C		      S		      2		      0		     1

1100 1001	1100 0011	0101 0011	1011 0010	0011 0000	1011 0001