Name: KEY									Id#

COE 205, Term 052

Computer Organization & Assembly Programming

Quiz# 2

Date: Monday, March 6, 2006

# Q1. Represent the numbers given below in Hexadecimal in the format specified in the table assuming 8-bits:

| Number | Sign-Magnitude | 1’s Complement | 2’s Complement |
| --- | --- | --- | --- |
| +20 | 14 | 14 | 14 |
| +108 | 6C | 6C | 6C |
| -20 | 94 | EB | EC |
| -108 | EC | 93 | 94 |

## Q2. Using the 2’s complement Hexadecimal representation obtained in Q1, perform the following operations and indicate if an overflow occurs or not:

i. (-108) - (20)

= 94 + EC

- 4

+ 	E   C

-----------

- 0

No overflow because we are adding two negative numbers and got a negative number.

ii. (108) + (-20)

= 6C + EC

- C

+ 	E   C

-----------

- 8

No overflow because we are adding positive and negative numbers.

## Q3. Determine the ASCII representation of the string AE31 assuming Even Parity. Note that the ASCII code of character A is 41H and that of character 0 is 30H.

A		         E		         3	    	        1

## 0100 0001	1100 0101	0011 0011	1011 0001