Name: KEY									Id#

COE 205, Term 061

Computer Organization & Assembly Programming

Quiz# 2

Date: Sunday, Oct. 8, 2006

# Q1. Consider an 8-bit register that has the binary number 11100100. Determine the decimal value of the number if it represents:

## An unsigned number.

= 128 + 64 + 32 + 4 = 228

## A signed number in sign-magnitude representation.

= -(64 + 32 + 4) = -100

## A signed number in 1’s complement representation.

We first take the 1’s complement = 00011011=16 + 8 + 2 + 1 = +27

Then, 11100100 = -27

## A signed number in 2’s complement representation.

We first take the 2’s complement = 00011100=16 + 8 + 4= +28

Then, 11100100 = -28

# Q2. Perform the following arithmetic operations assuming that numbers are represented using 8-bit 2’s complement representation. Indicate in your answer when an overflow occurs. Also determine the decimal value of the operands and the result

## 7F + FF

7F	(+127)

+	FF	(-1)

-----------------------------

7E	(+126)

No overflow since we are adding numbers of opposite sign.

## ii. 1E – 90 = 1E + 70

1E	(+30)

+	70	(+122)

-----------------------------

7E	(-114)

There is overflow since we are adding two positive numbers and we are getting a negative number.

# Q3. Fill the blanks in the following questions:

## (i)  The binary number 01100111 represents character ______g_____, and uses an ____odd____ parity bit. Note that the ASCII code of character A is 41H and that of character a is 61H.

## (ii) Assuming 6-bit 2`s complement representation, the smallest (negative) number is _____100000___ in binary and __-32____ in decimal and the largest (positive) number is _____011111___ in binary and ___+31____ in decimal.

# (iii)  If you type the characters A8c on your keyboard, the binary sequence sent to the computer using 8-bit ASCII code with the 8th bit being an even parity bit is 0100 0001(A)  1011 1000(8) 0110 0011(c). Note that the ASCII code for character 0 is 30H.