Name: KEY									Id#

COE 205, Term 062

Computer Organization & Assembly Programming

Quiz# 2

Date: Saturday, March 17, 2007

# Q1. Fill the blank in each of the following questions:

## The CPU is interfaced with memory and input/output devices through the address bus, data bus and control bus.

## The CPU consists mainly of the data path  unit and the control unit.

## If the clock period of a CPU is 0.5 ns, then its clock frequency is 2 GHz.

## A CPU with a 32-bit address bus has 4 GByte physical address space.

## With a data bus size equal to 64 bits, the maximum number of bytes that is transferred between the CPU and memory per a read/write cycle is   8  Bytes.

## The RAM is faster than hard disk and slower than cash memory.

## The disk access time is equal seek time + rotation latency + transfer time.

## The size of the address bus in the 8086 processor is 20 bits while in the Pentium IV Processor it is 36 bits.

## The size of the data bus in the 8086 processor is 16 bits while in the Pentium IV Processor it is 64 bits.

## CISC stands for Complex Instruction Set Computer while RISC stands for Reduced Instruction Set Computer.

## The IA-32 registers consist of 8 32-bit general-purpose registers, 6 16-bit segment registers, the EIP register and the EFLAGS register.

## Adding the following two 8-bit numbers FE+D5 has the following values on the flags: CF=1, ZF=0, SF=1, AF=1, PF=0, OF=0.

FE + D5 = D3 = 1101 0011

## The Instruction Register (IR)  holds the fetched instruction to be executed.

## The Instruction Pointer (IP) register holds the address of the next instruction to be fetched from memory.

## After reading an instruction whose size is 32 bits, the instruction pointer is incremented by    4.

## The instruction fetch-execute cycle can be divided into five stages: instruction fetch, instruction decode, operand fetch, execute, and write back result

## Pipelining makes its possible to start an instruction before completing the execution of previous one.

## In real address mode, the staring address of segment#F005 is F0050 and the maximum ending address is FFFFF.

F0050+0FFFF = 0004F. Since it exceeds the largest address, the maximum address allowed  is FFFFF.

## In real address mode with a logical address given as 2305:15F9, the linear address is 24649.

23050 + 015F9 = 24649

## In protected mode, linear address is translated to physical address using Paging.