Name: KEY									Id#

COE 205, Term 082

Computer Organization & Assembly Programming

Quiz# 2

Date: Monday, March 23, 2009

# Q1. Consider an 8-bit register that has the binary number 10010110. Determine the decimal value of the number if it represents:

## An unsigned number.

= 128+16+4+2=150

## A signed number in 2’s complement representation.

The 2's complement of 10010110 is 01101010.

The number 01101010 = 64+32+8+2 = 106.

Thus, the number 10010110 represents -106.

# Q2. Perform the following arithmetic operations assuming that numbers are represented using 8-bit 2’s complement representation. Indicate in your answer when an overflow occurs.

## CB + CA

CB + CA = 95.

There is no overflow since we are adding two negative numbers and we got a negative number.

## 68 – E0

# 68 – E0 = 68 + 20 = 88

There is overflow since we are adding two positive numbers and we got a negative number.

# Q3. Fill the blanks in the following questions:

## Assuming unsigned number representation, the hexadecimal number (8F)16 represents the decimal number 143.

## The decimal number 120 is represented in binary as 1111000.

## The binary number 11000111 represents character G and uses an odd parity bit. Note that the ASCII code of character A is 41H and that of character a is 61H.

## Assuming 8-bit 2`s complement representation, the smallest (negative) number is 10000000 in binary and -128 in decimal and the largest (positive) number is 01111111 in binary and +127 in decimal.