Name:									Id#

COE 205, Term 003

Computer Organization & Assembly Programming
Quiz# 3

Date: Sunday, July 22

# Q1. Give a single logic instruction to do each of the following:

## Convert the ASCII code of the character stored in AL from lower case to upper case. Note that the ASCII code of ‘A’=41h and the ASCII code of ‘a’=61h.

## Convert the number stored in DX to the closest even number that is smaller or equal to that in DX.

## c.   Replace the content of the word pointed by SI by its one`s complement.

# Q2. Write an 8086 assembly code to implement the following assuming that registers contain signed numbers:

For (I=-5; I<5; I++)

IF AX >= BX THEN

BX=BX*2;

ELSE

IF (BX < CX) AND (BX < DX) THEN

AX=AX+1

ELSE

DX=DX/2

END_IF

END_IF

END_FOR

# Q3. Suppose that register AX=8BEDh, CX=FF44h and the carry flag is 0. Determine the content of register AX and the carry flag after executing the following instruction:

# ROR AX, CL

# Q4. Write an 8086 assembly program to multiply the signed content of register AL by 19.25 based on shift and addition instructions using the smallest number of instructions possible.