Name:									Id#

COE 205, Term 021

Computer Organization & Assembly Programming

Quiz# 3

Date: Saturday, Oct. 9, 2002

# Q1. Give a single logic instruction to do each of the following:

## Convert the decimal digit (0-9) stored in register AL to its corresponding character. Note that the ASCII code of ‘0’=30h.

## Check if the number stored in register AL is even or odd.

## c.   Complement the odd bits in register AL while leaving the even bits unchanged.

# Q2. Write an assembly program to multiply the signed content of register AL by 28.5 based on shift and addition/subtraction instructions using the smallest number of instructions possible.