Name:									       Id#

COE 205, Term 033

Computer Organization & Assembly Programming

Quiz# 3

Date: Sunday, July 11, 2004

## Q1. Suppose that the following data segment is allocated in the segment given in the DS register with an offset of 0. Show the content of the allocated memory, in hexadecimal.  Note that the ASCII code of character ‘A’ is 41H and that of ‘a’ is 61H. The ASCII code of ‘$’ character is 24H.

I 	DB	112, -112, ‘CD’

J	DW	256, 0EH

K          EQU    23

L	DW	J+K

DD	offset I+20

Sname  DB	5, 6  dup(‘$’)

| Variable | Memory Address (Hex) | Memory Content Hex) |
| --- | --- | --- |
|  | 0000 |  |
|  | 0001 |  |
|  | 0002 |  |
|  | 0003 |  |
|  | 0004 |  |
|  | 0005 |  |
|  | 0006 |  |
|  | 0007 |  |
|  | 0008 |  |
|  | 0009 |  |
|  | 000A |  |
|  | 000B |  |
|  | 000C |  |
|  | 000D |  |
|  | 000E |  |
|  | 000F |  |
|  | 0010 |  |
|  | 0011 |  |
|  | 0012 |  |
|  | 0013 |  |
|  | 0014 |  |
|  | 0015 |  |
|  | 0016 |  |

## Q2.  Write a program to ask the user to enter a character in upper case and in a new line print the character  in both upper case and lower case.

## Q3.  Define a variable called Iname to be used for reading initial names of students such that the maximum allowed size is 15 characters for each name. Then show the code that will be used for reading a single name using INT 21H.