Name:									       Id#

COE 205, Term 042

Computer Organization & Assembly Programming

Quiz# 3

Date: Tuesday, March 15, 2005

## Q1. Suppose that the following data segment is allocated in the segment given in the DS register with an offset of 0. Show the content of the allocated memory, in hexadecimal.  Note that the ASCII code of character ‘A’ is 41H and that of ‘a’ is 61H.

I 	DB	-14, 100, ‘200’

J	DW	255, 1CH

K          EQU    2

L	DW	J-K

DD	offset I+16

M         DB	2, 2  dup(1,2)

| Variable | Memory Address (Hex) | Memory Content Hex) |
| --- | --- | --- |
|  | 0000 |  |
|  | 0001 |  |
|  | 0002 |  |
|  | 0003 |  |
|  | 0004 |  |
|  | 0005 |  |
|  | 0006 |  |
|  | 0007 |  |
|  | 0008 |  |
|  | 0009 |  |
|  | 000A |  |
|  | 000B |  |
|  | 000C |  |
|  | 000D |  |
|  | 000E |  |
|  | 000F |  |
|  | 0010 |  |
|  | 0011 |  |
|  | 0012 |  |
|  | 0013 |  |
|  | 0014 |  |
|  | 0015 |  |
|  | 0016 |  |

## Q2.  Given the following data declarations, determine what is printed by each of the following statements. Note that the ASCII code for the Line Feed character is 10 and that for the Carriage Return is 13:

MSG  		DB “Ali”,13, “Ahmad”, 10, “ Khaled”, 0DH, 0AH

MSG2 		DB “Samy $”

MSG3 		DB “Waleed”, “$”

- MOV AH, 2

MOV DL, MSG2[2]

INT 21H

- MOV AH, 9

MOV DX, Offset MSG

INT 21H

- MOV AH, 9

LEA DX, MSG3+2

INT 21H