Name:									       Id#

COE 205, Term 051

Computer Organization & Assembly Programming

Quiz# 3

Date: Saturday, Oct. 8, 2005

## Q1. Suppose that the following data declarations are allocated in the segment given in the DS register with an offset of 0. Show the content of the allocated memory, in hexadecimal.  Note that the ASCII code of character ‘A’ is 41H and that of ‘a’ is 61H. Also, the ASCII code of character ‘0’ is 30H.

I 	DB	-5,  ‘3AH’

J	DW	3AH

K          EQU    100

L	DW	K+1

DD	offset I-1

M         DB	5, 3  dup(-1,1)

| Variable | Memory Address (Hex) | Memory Content Hex) |
| --- | --- | --- |
|  | 0000 |  |
|  | 0001 |  |
|  | 0002 |  |
|  | 0003 |  |
|  | 0004 |  |
|  | 0005 |  |
|  | 0006 |  |
|  | 0007 |  |
|  | 0008 |  |
|  | 0009 |  |
|  | 000A |  |
|  | 000B |  |
|  | 000C |  |
|  | 000D |  |
|  | 000E |  |
|  | 000F |  |
|  | 0010 |  |
|  | 0011 |  |
|  | 0012 |  |
|  | 0013 |  |
|  | 0014 |  |
|  | 0015 |  |
|  | 0016 |  |

## Q2.  Determine the output produced by the given program assuming that it receives character ‘A’ as an input. Note that the ASCII code for the Line Feed character is 10 and that for the Carriage Return is 13:

.model small

.stack 100h

.data

LF EQU 10

CR EQU 13

MSG DB ‘Enter a character:$’

NLINE DB 10, 13, ‘$’

CHAR DB ?, LF,’$’

.code

.startup

MOV AH, 9

MOV DX, offset MSG

INT 21H

MOV AH, 1

INT 21H

MOV CHAR, AL

MOV AH, 9

LEA DX, NLINE

INT 21H

MOV CX, 5

LEA DX, CHAR

Next:		INT 21H

INC CHAR

LOOP Next

.exit

END