Name: KEY									Id#

COE 205, Term 032

Computer Organization & Assembly Programming

Quiz# 3

Date: Sunday, March 14, 2004

## Q1. Suppose that the following data segment is allocated in the segment given in the DS register with an offset of 0. Show the content of the allocated memory, in hexadecimal.  Note that the ASCII code of character ‘A’ is 41H and that of ‘a’ is 61H.

I 	DB	-2, 250, ‘Ab’

DW	3AaH, `Cd`

L          EQU    16

J	DD	L-17

DW	offset I+10

K         DB	2 dup( 3dup(-16,’a’))

| Variable | Memory Address (Hex) | Memory Content Hex) |
| --- | --- | --- |
| I | 0000 | FE |
|  | 0001 | FA |
|  | 0002 | 41 |
|  | 0003 | 62 |
|  | 0004 | AA |
|  | 0005 | 03 |
|  | 0006 | 64 |
|  | 0007 | 43 |
| J | 0008 | FF |
|  | 0009 | FF |
|  | 000A | FF |
|  | 000B | FF |
|  | 000C | 0A |
|  | 000D | 00 |
| K | 000E | F0 |
|  | 000F | 61 |
|  | 0010 | F0 |
|  | 0011 | 61 |
|  | 0012 | F0 |
|  | 0013 | 61 |
|  | 0014 | F0 |
|  | 0015 | 61 |
|  | 0016 | F0 |
|  | 0017 | 61 |
|  | 0018 | F0 |
|  | 0019 | 61 |

## Q2.  Given the following data declarations, determine what is printed by each of the following statements. Note that the ASCII code for the Line Feed character is 10 and that for the Carriage Return is 13:

MSG   DB “Hello”,10, “ COE 205 ”, 10, “ Q2 ”, “$”

MSG2 DB “Hello”,13, “ COE 205 ”,13, “ Q2 ”

MSG3 DB “ Quiz#3  ”, “$”

- MOV AH, 2

MOV DL, MSG2

INT 21H

H

- MOV AH, 2

MOV DL, MSG2-1

INT 21H

$

- MOV AH, 9

MOV DX, Offset MSG

INT 21H

Hello

COE 205

Q2

- MOV AH, 9

LEA DX,  MSG2

INT 21H

Q2  Quiz#3