Name:									       Id#

COE 205, Term 033

Computer Organization & Assembly Programming

Quiz# 3 Solution

Date: Sunday, July 11, 2004

## Q1. Suppose that the following data segment is allocated in the segment given in the DS register with an offset of 0. Show the content of the allocated memory, in hexadecimal.  Note that the ASCII code of character ‘A’ is 41H and that of ‘a’ is 61H. The ASCII code of ‘$’ character is 24H.

I 	DB	112, -112, ‘CD’

J	DW	256, 0EH

K          EQU    23

L	DW	J+K

DD	offset I+20

Sname  DB	5, 6  dup(‘$’)

| Variable | Memory Address (Hex) | Memory Content Hex) |
| --- | --- | --- |
| I | 0000 | 70 |
|  | 0001 | 90 |
|  | 0002 | 43 |
|  | 0003 | 44 |
| J | 0004 | 00 |
|  | 0005 | 01 |
|  | 0006 | 0E |
|  | 0007 | 00 |
| L | 0008 | 1B |
|  | 0009 | 00 |
|  | 000A | 14 |
|  | 000B | 00 |
|  | 000C | 00 |
|  | 000D | 00 |
| Sname | 000E | 05 |
|  | 000F | 24 |
|  | 0010 | 24 |
|  | 0011 | 24 |
|  | 0012 | 24 |
|  | 0013 | 24 |
|  | 0014 | 24 |
|  | 0015 |  |
|  | 0016 |  |

## Q2.  Write a program to ask the user to enter a character in upper case and in a new line print the character  in both upper case and lower case.

.model small

.stack 100

.data

MSG DB ‘Enter a character in upper case:$’

NL     DB  10, 13, ‘$’

.code

.startup

; printing the first message

MOV AH, 9

MOV DX, offset MSG

INT 21H

;reading the upper case character

MOV AH, 1

INT 21H

MOV BL, AL

; printing a new line

MOV AH, 9

MOV DX, offset NL

INT 21H

;printing the upper case character

MOV AH, 2

MOV DL, BL

INT 21H

; printing the lower case character

ADD DL, 20h

INT 21h

.exit

END

## Q3.  Define a variable called Iname to be used for reading initial names of students such that the maximum allowed size is 15 characters for each name. Then show the code that will be used for reading a single name using INT 21H.

Iname DB 16, 17 dup(?)

;to read a name into Iname

MOV AH, 10

MOV DX, offset Iname

INT 21H