Name: KEY									Id#

COE 205, Term 071

Computer Organization & Assembly Programming

Quiz# 3

Date: Saturday, Nov. 17, 2007

# Q1. Suppose that you have the following initial content of registers and stack memory after fetching each of the instructions shown below:

EAX=00001F20H   EBX=FFFFFC55H   ESP=00001000H    EIP=000030B0H

# Determine the content of ESP, modified registers, and modified stack memory locations after the execution of each of the following instructions starting from the initial content of the registers and memory for the execution of each instruction.

| Memory Location | Content |
| --- | --- |
| 00000FFC | 20 |
| 00000FFD | 30 |
| 00000FFE | 40 |
| 00000FFF | 50 |
| 00001000 | 60 |
| 00001001 | 70 |
| 00001002 | 80 |

# PUSH EAX.

ESP = ESP – 4 = 1000 – 4 = 00000FFC

[FFFF:FFFC]=00001F20

# POP BX.

BX=[1001:1000] = 7060

ESP = ESP + 2 = 1000 + 2 = 00001002

# Q2. You are required to write a program to display a given column of a two-dimensional array of unsigned integers, TARRY. Assume that each integer is stored in a double word. To do that you need to do the following:

# Ask the user to enter the number of rows.

# Ask the user to enter a column number.

# In a new line, print the selected column.

Note that the procedure WriteDec can be used for displaying the content of EAX in unsigned decimal format to standard output. The procedure WriteString writes a null-terminated string whose address is stored in EDX to standard output.  The procedure WriteChar writes the character in register AL to standard output.  The procedure Crlf writes end of line sequence (CR, LF) to standard output. The procedure ReadDec reads a 32-bit unsigned integer and returns it in EAX. You only need to show the data and code segments of the program.

A sample execution of the program for the array given below is shown:

TARRAY 	DWORD 1, 5, 300, 100, 5000

DWORD 600, 0, 1110, 2000, 2

DWORD 99, 16, 150, 530, 440

Enter the number of rows: 3

Enter a column number: 1

Column # 1

5

0

16

.DATA

MSG  BYTE "Enter the number of rows: ",0

MSG2 BYTE "Enter a column number: ",0

MSG3 Byte "Column#",0

TARRAY DWORD 1, 5, 300, 100, 5000

DWORD 600, 0, 1110, 2000, 2

DWORD 99, 16, 150, 530, 440

.CODE

main PROC

MOV EDX, offset MSG

Call WriteString

Call ReadDec

MOV ECX, EAX

MOV EDX, offset MSG2

Call WriteString

Call ReadDec

MOV EBX, EAX

MOV EDX, offset MSG3

Call WriteString

Call WriteDec

Call CRLF

Next:

MOV EAX, TARRAY[EBX*Type TARRAY]

Call WriteDec

Call CRLF

ADD EBX, lengthof TARRAY

Loop Next

main ENDP

END main