Name:									Id#

COE 205, Term 991

Computer Organization & Assembly Programming
Quiz# 4

Date: Wednesday, May. 10

# Q1. Consider the one-bus CPU organization shown below. Assume that the CPU has  only three general registers, namely R0, R1, and R2. Furthermore, assume that the ALU can perform any of the following four functions based on the control signals f1, f2, f3, and f4, as shown below:

# f1: C=A+B;	  	f2: C=A-B;		f3: C=A+1; 		f4: C=A-1;

- Write the minimum number of control steps required to fetch an instruction using this CPU. Assume that the memory is asynchronous and that each instruction occupies one memory location.

- Write the minimum number of control steps required to execute each of the following instructions:

- SUB R1, 20	; subtract the constant value 20  from R1 and store the result in R1.

- INC J		; increment the content of memory variable J.

- MOV I, R1 	; move the content of register R1 to memory variable I;

- LOOP label	; decrement content of R0 and then branch conditionally to            label if the zero flag equals to 0. The branch address is specified using relative addressing mode.

- Assuming  that the instruction set of the CPU consists of only the four instructions mentioned above, determine  the logic needed in the encoder of a hardwired control unit for the signal MARin.

Q2. Consider the CPU-Memory interface circuit shown below. Complete the timing diagram of the read operation shown below.

# Text boxes

CLK

Read

WMFC

MFC

MR

Run