Name:									Id#

COE 205, Term 033

Computer Organization & Assembly Programming

Quiz# 4 Solution

Date: Tuesday, July 20, 2004

# Q1. Suppose that you have the following initial content of 8086 registers:

AX=00F7H		BX=0004H		CX=FFF2H		DX=0000H

## Determine the content of the destination operand after the execution of each of the following instructions. Indicate the effect on the overflow flag. Use the initial content of the registers for the execution of each instruction.

### MUL BL

AX = F7 * 04 = 03DC

OF =1 since the result does not fit in AL i.e. AH is not equal to 0.

### IMUL BL

AX = F7 * 04 = -9*4 =-36 = FFDC  (note that 36=0024)

OF =0 since the result fits in AL i.e. AH is a sign-extension of AL.

### DIV BX

### We are dividing DX:AX over BX => 0000:00F7 / 0004

This gives a quotient of 003D and a remainder of 0003. So, DX=0003 and 			        AX=003D.

OF is undefined.

### IDIV CX

### We are dividing DX:AX over CX => 247 / -14

This gives a quotient of -17 and a remainder of 9. So, DX=0009 and 			        	        AX=FFEF.

OF is undefined.