Name: Key									Id#

COE 205, Term 042

Computer Organization & Assembly Programming

Quiz# 4

Date: Tuesday, April 5, 2005

# Q1. Suppose that you have the following initial content of 8086 registers:

AX=FFF0H		BX=0008H		CX=FFF2H		DX=2010H

## Determine the content of the destination operand after the execution of each of the following instructions. Indicate the effect on the overflow flag. Use the initial content of the registers for the execution of each instruction.

### MUL BL

AX = 0780	CF=OF=1

### IMUL BL

AX =FF80	CF=OF=0

(ii) Write 8086 assembly code to display the decimal content of register AX assuming unsigned numbers.

.model small

.stack 100h

.data

num db 0,0,0,0,0,'$'

.code

.startup

MOV CX, 5

MOV SI, 4

MOV BX, 10

Next:   XOR DX, DX

DIV BX

ADD DL, '0'

MOV num[SI], DL

DEC SI

Loop Next

MOV AH, 9

LEA DX, num

INT 21H

.exit

end