Name:   KEY									Id#

COE 205, Term 043

Computer Organization & Assembly Programming

Quiz# 4

Date: Tuesday, July 26, 2005

# Q1. Suppose that you have the following initial content of 8086 registers:

AX=FFDFH		BX=0008H		CX=0020H		DX=0001H

## Determine the content of the destination operand after the execution of each of the following instructions. Indicate the effect on the overflow flag. Use the initial content of the registers for the execution of each instruction.

### MUL BX

DX:AX=AX * BX ;  DX=0007  AX=FEF8;  OF=1 because DX is not 0.

### IMUL AH

AX=AL*AH; 	  AX=0021;  OF=0 because AH is a sign extension of AL.

### DIV BX

DX:AX= DX:AX/BX;   DX=0007   AX=3FFB;   OF is undefined

### IDIV CL

AH:AL= AX/CL=-33/32;   AH=FF   AL=FF	;   OF is undefined

(ii) Write the minimum number of instructions to do the following using only logical instructions:

### Clear bit 0, Set bit 7, and Complement bit 4 of register AL.

AND AL, 11111110B   	Another solution:

OR  AL, 10000000B		 AND AL,01111110B

XOR AL, 00010000B		 XOR AL,10010000B

### Change the content of AL register into UPPER case assuming that it contains either upper or lower case alphabetic characters.

AND AL, 1101111B

### Store the content of register CX into register AX using only XOR instructions.

XOR AX, AX;	AX=0

XOR AX, CX; 	AX = 0 XOR CX = CX