Name: KEY									       Id#

COE 205, Term 052

Computer Organization & Assembly Programming

Quiz# 4

Date: Saturday, April 8, 2006

## Q1. Suppose that you have an array of 10 bytes as defined below:

Array DB 1, 20, 15, 4, -6, 22, -50 99, 100, -10

You are required to write a program to do the following:

- Compute the square of each number in the array and store the result in another array called SQArray.

- Compute the result of dividing each number by 3 and store the Quotients in QArray and the remainders in RArray.

.model small

.stack 100h

.data

Array DB 1, 20, 15, 4, -6, 22, -50 99, 100, -10

SQArray DW 10 DUP(?)

QArray DB 10 DUP(?)

RArray DB 10 DUP(?)

.586

.code

.Startup

MOV CX, 10

XOR ESI, ESI

Next:	MOV AL, Array[ESI]		; getting a number from the array

MOV BL, AL

IMUL AL			; compute the square of a number

MOV SQArray[ESI], AX	; store the square

MOVZX AX, BL		; get the number to be divided

MOV BL, 3

IDIV BL			; perform divition by 3

MOV Rarray[ESI], AH	; store the reminder

MOV Qarray[ESI], AL	; stoe the quotient

INC ESI

LOOP Next

.EXIT

END