Name: KEY									Id#

COE 205, Term 071

Computer Organization & Assembly Programming

Quiz# 4

Date: Saturday, Nov. 24, 2007

# Q1.  You required to write a procedure, COPY, that copies one array into another. The addresses of the two arrays, their length and type should be passed as parameters on the stack. The procedure should preserve all used registers and should free all parameters upon return. Use the procedure COPY to copy Array1 into Array2 assuming that they are declared as arrays of 100 words.

.DATA

Array1 Word 10 DUP (20)

Array2 Word 10 DUP (0)

.CODE

main PROC

LEA EAX, Array1

PUSH EAX

LEA EAX, Array2

PUSH EAX

MOV EAX, lengthof Array1

PUSH EAX

MOV EAX, Type Array1

PUSH EAX

CALL COPY

exit	; exit to operating system

main ENDP

COPY PROC

PUSH EBP

MOV EBP, ESP

PUSHAD                  ; saving registers

MOV EAX, [EBP+8]        ; array type

MOV ECX, [EBP+12]       ; length of array

MUL ECX                 ; EAX contains number of bytes to be copied

MOV ECX, EAX

MOV EDI, [EBP+16]       ; address of destination array

MOV ESI, [EBP+20]       ; address of source array

MOV EAX, 0

Next:

MOV BL, [ESI+EAX]

MOV [EDI+EAX], BL

INC EAX

LOOP Next

POPAD                   ; restoring registers

POP EBP              ; restore EBP

RET 16

COPY ENDP

END main