Name:									Id#

COE 205, Term 071

Computer Organization & Assembly Programming

Quiz# 5

Date: Saturday, Dec. 8, 2007

Q1. Write the minimum number of instructions to do the following using only logical instructions:

### Clear bit 0, Set bit 7, and Complement bit 4 of register AL.

### Store the content of register CX into register AX using only XOR instructions.

# Q2. Given that TABLE is defined as: TABLE db ‘This Is Not Difficult’

## Determine the content of register AL after executing the following code and describe briefly what the code is doing:

## MOV ECX, lengthof TABLE

XOR AL, AL

LEA EBX, TABLE

DEC EBX

Next: 	JECXZ ENL

INC EBX

MOV AH,  [EBX]

OR AH, 20h

CMP AH, 'i'

LOOPNE Next

JNE  ENL

INC AL

JMP Next

ENL:

# Q3. Write an assembly program to implement the following code assuming that unsigned numbers are represented in registers:

WHILE (AX ( 0) {

IF (BX < CX) OR (BX <= 100) {

BX = BX + DX;

} ELSE {

BX = BX – 2;

}

AX = AX – 1;

}