Name: Key									Id#

COE 205, Term 022

Computer Organization & Assembly Programming

Quiz# 5

Date: Sunday, Apr. 27, 2003

# Q1. Based only on logic instructions, do each of the following:

## Convert the decimal digit (0-9) stored in register AL to its corresponding character. Note that the ASCII code of ‘0’=30h.

## OR AL, 30H

## Check if the number stored in register AL is even or odd.

TEST AL, 1

JZ Even

## c.   Convert a lower case character in AL to upper case and upper case character to lower case.

## XOR AL, 20H

# Q2. Write an assembly program to multiply the signed content of register AL by 48.5 based on shift and addition/subtraction instructions using the smallest number of instructions possible.

# MOV AH, AL

MOV CL,  4

SAL AL, CL		; AL = 16 AL

MOV DL, AL		; DL = 16 AL

SAL AL, 1		; AL = 32 AL

ADD AL, DL		; AL = 48 AL

SAR AH, 1		; AH = 0.5 AL

ADD AL, AH		; AL = 48.5 AL