Name: KEY									Id#

COE 205, Term 031

Computer Organization & Assembly Programming

Quiz# 5

Date: Sunday, Dec. 14, 2003

# Q1. Write a procedure to display the binary content of an 8-bit register. Assume that the 8-bit value to be displayed is passed on the stack. Then show how to use the procedure to display the content of register AL

DISPB PROC

;reading the parameter from the stack

MOV BP, SP

MOV AX, [BP+2]

; displaying the biary content of register AL

MOV AH, 2

MOV CX, 8

Next:   MOV DL, 30H

ROL AL, 1

ADC DL, 0

INT 21H

LOOP Next

RET 2

DISB ENDP

# Q2. Write a macro to display the binary content of an 8-bit register. Assume that the 8-bit register to be displayed is given as a parameter to the macro. Then, show how to use the macro to display the content of register AL

# DISPBM MACRO	 reg8

Local Next

MOV AL, reg8

MOV AH, 2

MOV CX, 8

Next:   MOV DL, 30H

ROL AL, 1

ADC DL, 0

INT 21H

LOOP Next

ENDM