Name: KEY									Id#

COE 205, Term 042

Computer Organization & Assembly Programming

Quiz# 5

Date: Sunday, April 24, 2005

# Q1. Write an 8086 assembly program to display the hexadecimal content of register AX. Do not use multiplication or division instructions. The content of register AX should remain the same.

.model small

.stack 100h

.data

Hextable DB '0123456789ABCDEF'

.386

.code

.startup

MOV AX, 1234h ; example to display

LEA BX, Hextable

MOV SI, AX

MOV CX, 4

Next:   ROL SI, 4

MOV AX, SI

AND AX, 0Fh

XLATB

MOV AH, 2

MOV DL, AL

INT 21H

LOOP Next

MOV AX, SI	; restore AX value

.exit

end