Name:  KEY									Id#

COE 205, Term 051

Computer Organization & Assembly Programming

Quiz# 5

Date: Monday, Nov. 28, 2005

# Q1. Suppose that you have the following initial content of 8086 registers:

AX=F504H		BX=7010H		CX=02F2H		DX=1234H

## Determine the content of the destination operand and the value of the carry flag after the execution of each of the following instructions. Use the initial content of the registers for the execution of each instruction.

### SHR AX, CL

Only the least significant 5 bits of CL will determine the amount of shift i.e.       the amount of shift = 17  => AX=0000 and CF=0.

### SAR AX, 2

AX=FD41		CF=0.

### ROL AX, 129

This is equivalent to ROL AX, 1 => AX=EA09 and CF=1.

### SHLD AX, BX, 4

AX=5047		CF=1. Note that BX does not change.

(ii) Write an 8086 assembly program using conditional loop instructions to count the number of non-blank characters in a Table of 80 characters.

MOV CX, 80

XOR AL, AL; AL will hold the number of non-blank char.

MOV SI, -1

Next:

JCXZ Done

INC SI

CMP Table[SI], ' '

LOOPE Next

JE Done

INC AL

JMP Next

Done: