Name: KEY									Id#

COE 205, Term 071

Computer Organization & Assembly Programming

Quiz# 5

Date: Saturday, Dec. 8, 2007

Q1. Write the minimum number of instructions to do the following using only logical instructions:

### Clear bit 0, Set bit 7, and Complement bit 4 of register AL.

AND AL,01111110B

XOR AL,10010000B

### Store the content of register CX into register AX using only XOR instructions.

# XOR AX, AX;	AX=0

XOR AX, CX; 	AX = 0 XOR CX = CX

# Q2. Given that TABLE is defined as: TABLE db ‘This Is Not Difficult’

## Determine the content of register AL after executing the following code and describe briefly what the code is doing:

## MOV ECX, lengthof TABLE

XOR AL, AL

LEA EBX, TABLE

DEC EBX

Next: 	JECXZ ENL

INC EBX

MOV AH,  [EBX]

OR AH, 20h

CMP AH, 'i'

LOOPNE Next

JNE  ENL

INC AL

JMP Next

ENL:

Content of AL=4. The program counts the number of character 'i' both upper and lower case.

# Q3. Write an assembly program to implement the following code assuming that unsigned numbers are represented in registers:

| WHILE (AX ( 0) { IF (BX < CX) OR (BX <= 100) { BX = BX + DX; } ELSE { BX = BX – 2; } AX = AX – 1; } | While: CMP AX, 0 JB EndWhile CMB BX, CX JB Then CMP BX, 100 JBE Then SUB BX, 2 JMP EndIf Then: ADD BX, DX EndIf: DEC AX JMP While EndWhile: |
| --- | --- |