Name:  									Id#

COE 205, Term 051

Computer Organization & Assembly Programming

Quiz# 6

Date: Monday, Dec. 10, 2005

# Q1. Suppose that you have the following initial content of registers and memory:

AX=1A22H	BX=3C40H	CX=4502H	SP=1000H	BP=1002H

Determine the content of SP, the modified stack locations and modified registers after the execution of each of the following instructions starting from the initial content of the registers and stack content for the execution of each instruction.

| Memory Location | Content |
| --- | --- |
| 0FFD | 1A |
| 0FFE | CF |
| 0FFF | 36 |
| 1000 | 1B |
| 1001 | 60 |
| 1002 | 32 |
| 1003 | FF |
| 1004 | E4 |

## PUSH AX

## POP BX

## POP ECX

## RET 2

# Q2. Determine the output displayed by executing the following code. Explain what the procedure DISPS does.

.model small

.stack 100h

.data

msg DB 'This is the last quiz in Assembly!!'

.code

.startup

LEA AX, msg

PUSH AX

MOV AX, 8

PUSH AX

CALL DISPS

.exit

DISPS PROC

MOV BP, SP

PUSH CX

PUSH SI

PUSH AX

PUSH DX

MOV CX, [BP+2]

MOV SI, [BP+4]

MOV AH, 2

Next:

MOV DL, [SI]

INT 21H

INC SI

LOOP Next

POP DX

POP AX

POP SI

POP CX

RET 4

DISPS ENDP

end