Name: KEY									Id#

COE 205, Term 032

Computer Organization & Assembly Programming

Quiz# 6

Date: Tuesday, May 4, 2004

# Q1. Write a macro, BDREG, to display the binary content of a register. Assume that name of the register and the number of bits in a register are passed as macro parameters.  Then, use the macro to display the binary content of register CX.

.model small

.stack 100h

BDREG MACRO reg, size

local next, mysize

JMP Next

mysize DB size

Next:

ROL reg, 1

PUSH AX

PUSH DX

MOV AH, 2

MOV DL, '0'

ADC DL, 0

INT 21H

POP DX

POP AX

DEC mysize

JNZ Next

ENDM

.code

.startup

; to display the CX register the following macro invocation is used

MOV CX, 10

BDREG CX, 16

.exit

END