Name:									Id#

COE 205, Term 033

Computer Organization & Assembly Programming

Quiz# 6 Solution

Date: Saturday, July 31, 2004

# Q1. Write a procedure, ReadBin, to read a binary number. The number of bits to be read is passed on the stack and it can be up to 16 bits. The read number should be returned on the stack.  The procedure should restore the status of all registers to their content before the procedure execution. Then, use the procedure to read an 8-bit binary number and store the result in AL. Show the complete program and the place of the procedure in the program. Do not use multiplication instructions in your solution.

.model small

.stack 100h

.code

.startup

MOV AX, 8

PUSH AX

CALL READBIN

POP AX

.exit

READBIN PROC

PUSH BP

MOV BP, SP

PUSH AX

PUSH BX

PUSH CX

MOV CX, [BP+4]

XOR BX, BX

MOV AH, 1

Next:   INT 21H

SHR AL, 1

RCL BX, 1

LOOP Next

MOV [BP+4], BX

POP CX

POP BX

POP AX

POP BP

RET

READBIN ENDP

END