Name:  KEY									Id#

COE 205, Term 043

Computer Organization & Assembly Programming

Quiz# 6

Date: Sunday, August 7, 2005

# Q1. Determine the content of register AX after executing the following code. Briefly describe the main functionality of the given procedure.

.model small

.data

MSG DB 'here is a test'

.code

.startup

LEA AX, MSG

PUSH AX

MOV AX, 14

PUSH AX

MOV AL, 'e'

PUSH AX

CALL MYPROC

.exit

MYPROC PROC

MOV BP, SP

PUSH BX

PUSH CX

PUSH SI

MOV BL, [BP+2]

MOV CX, [BP+4]

MOV SI, [BP+6]

XOR AX, AX

NEXT:   INC SI

CMP BL, [SI-1]

LOOPNE NEXT

JNE DONE

INC AX

JCXZ DONE

JMP NEXT

DONE:   POP SI

POP CX

POP BX

RET 6

MYPROC ENDP

END

The content of register AX is 3. The procedure gets as parameters the address of a string, the length of the string and a character for which it counts the number of its occurrences in the string. Since the character  is ‘e’ the procedure finds that it occurs 3 times and returns 3 in AX.