Name: KEY									       Id#

COE 205, Term 052

Computer Organization & Assembly Programming

Quiz# 6

Date: Monday, May 1, 2006

## Q1.

- Write a procedure that receives the address of a string and the its size from the stack and prints it. The procedure should preserve the content of all registers changed during its implementation except the BP register.

- Write a program to use the procedure to print the string “This is an Easy Test !!”.  Show the place of the procedure definition in the program.

(i)

DISPLAY PROC Near

MOV BP, SP

; saving used registers

PUSH AX

PUSH BX

PUSH CX

PUSH DX

; getting the parameters fro teh stack

MOV CX, [BP+2]

MOV BX, [BP+4]

; printing the string

MOV AH, 2

Next:

MOV DL, [BX]

INT 21H

INC BX

LOOP Next

; restoring used registers

POP DX

POP CX

POP BX

POP AX

RET 4

DISPLAY ENDP

(ii)

.mode small

.data

MSG DB  “This is an Easy Test !!”

.code

.startup

; passing parameters on stack

LEA AX, MSG

PUSH AX

MOV AX, 22

PUSH AX

; calling procedure

CALL DISPLAY

.exit

; procedure is defined here

END