COE 464, Term 042

Testing of Digital Circuits

HW#3

Due date: Sunday, April 17

# Consider the circuit shown in Figure 5.26(a) for a full-adder.  Furthermore, consider the fault N s-a-0 in the circuit.

## Generate a test for the fault using the D algorithm. Show all the details of the algorithm including the D-Frontier, the J-Frontier and the Decision tree. Whenever there are choices, select the choices in ascending alphabetical order.  Verify your result by fault simulating the derived test using either PROOFS or HOPE.

## Generate a test for the fault using the PODEM algorithm. Show all the details of the algorithm including the D-Frontier and the Decision tree. Whenever there are choices, select the choices in ascending alphabetical order.  Verify your result by fault simulating the derived test using either PROOFS or HOPE.

## Generate a test for this fault using HITEC and compare the obtained test to your solution.