Name:									Id#

COE 464, Term 042

Testing of Digital Circuits

Quiz# 2

Date: Tuesday, March 15, 2005

# Q1. Consider the sequential circuit shown below, where Y is a primary output and X is a primary input:

## Show an iterative array model of two time frames for this circuit.

## Derive a test sequence for detecting the fault Y s-a-0.

## Consider the fault X s-a-0. Show the state tables of the fault-free and faulty machines. Is the fault detectable, strongly detectable, partially testable or redundant?  Justify your answer.

# Text boxes

Y

X

G4

G3

G2

G1

Q1

D1

Q0

G5

D0