Name:									Id#

COE 464, Term 042

Testing of Digital Circuits

Quiz# 6

Date: Sunday, May 29, 2005

# Q1. Consider the sequential circuit shown below, which has four primary inputs, namely I1, I2, I3, I4, and one primary output, Z, and four D-FFs

## Convert the given sequential circuit into a Full-Scan circuit using Multiplexed-Data Flip Flop (MD-FF) scan cell.

## Using the full-scan circuit derived in (i), generate a test for the fault G7 stuck-at-1.

# Text boxes

Z

G10

F2

G3

I2

I3

I1

G1

F1

G2

G4

G6

F3

G9

I4

G8

G7

G5

F4