May 29, 2003

COMPUTER ENGINEERING DEPARTMENT

COE 545

Digital System Testing

Major Exam II

Second Semester 2003 (022)

Time: 3:30-5:30 PM

Student Name : ______________________________________________

Student ID.     : ______________________________________________

| Question | Max Points | Score |
| --- | --- | --- |
| I | 30 |  |
| II | 30 |  |
| III | 20 |  |
| IV | 20 |  |
| Total | 100 |  |

Dr. Aiman El-Maleh

[30 Points]

# (I) Consider the circuit shown below:

## Compute the controllability and observability costs for every line in the circuit using the generalized formulas (6.1) to (6.4).

## Determine a lower bound on the detection probability of the stuck-at 0 fault on the stem B based on fault propagation across the path {G4, G5}.

## What is the exact detection probability of the fault?

## Based on the exact fault detection probability obtained in (c), compute the escape probability of the fault assuming that 10 random vectors are applied.

## What is the length of random test patterns required such that the escape probability of any fault in the circuit is less than or equal to 10-2? Hint: consider the faults on node g.

[30 points]

# (II) Consider the circuit shown below:

## Generate a test vector to detect the stuck-at-1 fault on the output of G3 using the following algorithms:

## 1. D-Algorithm.

## 2. PODEM.

## Show the detailed steps done by each of the algorithms including the decision tree. Assume that the observability cost of G7<G6<G5<G4. Furthermore, assume that the controllability costs of A<B<C<D<G1<G2<G3<G4<G5<G6<G7.

[20 points]

# (III) Determine the following:

## The signal probability PZ of a 3-input OR gate Z=A+B+C as a function of its input signal probabilities, PA, PB, and PC. Assume that the inputs are independent.

## The signal probability PZ of a 2-input XOR gate Z=A XOR B as a function of its input signal probabilities, PA and PB. Assume that the inputs are independent.

## The primitive cubes and the propagation D-cubes of a gate G implementing the function G = A B + A C.

[20 points]

# (IV) Consider the sequential circuit shown below, where the sequential elements are D-FFs, I1 and I2 are primary inputs and Y is a primary output:

## Generate a minimal-length test sequence for detecting the single fault G2 stuck-at-1 assuming the reset state 000.

## Generate a minimal-length self-initializing test sequence for detecting the single fault G2 stuck-at-1.

# Text boxes

G3

G14

CLK

Q1

D1

CLK

G3

Q2

B

A

D2

G2

C

G1

G2

G1

G2

G8

B

A

G5

D

C

G7

G6

B

G4

G3

A

D3

Q3

CLK

I2

I1

Y

G4

G5

C

D

e

f

g

h

i

j

k

l

m

n