(vii) Fault Collapsing using HITEC:

| Circuit Netlist INPUT(a) INPUT(b) OUTPUT(l) g = NAND(a, b) j = NAND(a, g) k = NAND(g, b) l = NAND(j, k) | Signal Names 1 a 2 b 3 g 4 j 5 k 6 l 7 l_$OUTPUT |
| --- | --- |
| Collapsed Faults 7 0 1 : 7 1 1 : 6 0 1 : 6 2 0 : 5 0 0 : 6 1 0 : 4 0 0 ; 5 2 1 ; 2 0 1 ; 5 1 1 ; 3 0 1 : 3 2 0 : 3 1 0 ; 2 0 0 ; 1 0 0 ; 4 2 1 ; 1 0 1 ; 4 1 1 ; 7 0 0 : 7 1 0 : 6 0 0 ; 6 2 1 : 5 0 1 : 5 2 0 : 5 1 0 ; 3 0 0 ; 3 2 1 ; 3 1 1 ; 6 1 1 : 4 0 1 : 4 2 0 : 4 1 0 ; Thus, we have the same set and number of collapsed faults based on equivalence fault collapsing. |

-4-

Verification using PROOFS fault simulator:

| Injected Fault 11 0 0 : 10 0 0; | Signal Names 1 X 2 Q0 3 Q1 4 G1 5 G2 6 G4 7 G6 8 G3 9 G5 10 Z 11 Z_$OUTPUT |
| --- | --- |
| Test Sequence 1 # This is number of inputs 0 1 1 0 END | Detection Statistics 0 user time 0.000000 sec sys time 0.016667 sec det faults 1 tot faults 1 coverage 1.000000 |

-6-

| Circuit Netlist INPUT(X) OUTPUT(Z) G1 = NOT(Q0) G2 = NOT(Q1) G3 = AND(X, G1, G2) G4 = OR(Q0, Q1) G5 = AND(G4, X) Q0 = DFF(G3) Q1 = DFF(G5) G6 = NOT(X) Z = AND(G6, Q1) | Signal Names 1 X 2 Q0 3 Q1 4 G1 5 G2 6 G4 7 G6 8 G3 9 G5 10 Z 11 Z_$OUTPUT |
| --- | --- |
| Injected Fault 1 0 1 ; | Detection Statistics BACKTRACK LIMIT 10000 STATE BACKTRACK LIMIT 10000 TIME LIMIT 2 system time 0.000 user time 0.000 total faults 1 detected faults 1 redundant finds 0 aborted faults 0 total vectors 4 efficiency 1.0000 coverage 1.0000 |
| Generate Test Sequence 1 # This is number of inputs 0 1 1 0 END |  |

Thus, we can see that the same test sequence was generated for detecting the fault x stuck-at-1.

-9-